## Slide 1: Smartphone Background Activities in the Wild: Origin, Energy Drain, and Optimization
Xiaomeng Chen
Abhilash Jindal
Ning Ding
Y. Charlie Hu
Maruti Gupta
Rath Vannihamby
Purdue University
Mobile Enerlytics
Intel Corporation

## Slide 2
Chart: 
| Fast processor | Well known brand | Long lasting batteries
Series 1 | 0.67 | 0.68 | 0.89
Important features to buy new phones
http://www.theguardian.com, May 2014
http://mobileenerlytics.com/blog/?p=14, Dec 2014
How often do users charge phones?

## Slide 3: Energy Measurement Study
Devices (> 10 days trace) | 2000
Unique phone types | Galaxy S3 & Galaxy S4
Median trace duration | 28 days
[1]eStar Energy Saver: https://play.google.com/store/apps/details?id=com.mobileenerlytics.estar
[2] Smartphone Energy Drain in the Wild: Analysis and Implications (Sigmetrics 2015)
Trace statistics [1]:
CPU
GPU
Screen
WiFi
3G/LTE
WiFi
beacon
WiFi
scan
Cellular
paging
SOC
suspension
Utilization-based
Finite State Machine
Constant
Hybrid power model [2]:

## Slide 4: Energy Measurement Study
Chart: 
| Maintenance energy during screen-off | Background apps and services during screen-off | CPU idle during screen-off | Screen-on
Energy | 17 | 22.9 | 6 | 54.1
46% screen-off energy

## Slide 5: Energy Measurement Study
Chart: 
| Maintenance energy during screen-off | Background apps and services during screen-off | CPU idle during screen-off | Screen-on
Energy | 17 | 22.9 | 6 | 54.1
17% maintenance energy

## Slide 6: Energy Measurement Study
Chart: 
| Maintenance energy during screen-off | Background apps and services during screen-off | CPU idle during screen-off | Screen-on
Energy | 17 | 22.9 | 6 | 54.1
29% energy due to background activities during screen-off
Reduce energy by optimizing background activities during screen-off
Notes: And the rest 29% energy is due to background activities of the installed apps.
This provide us a good opportunity to reduce energy from background activities during screen-off

## Slide 7: Screen-off Activities
Pre-fetch updates
Notifications
Non-touch based user interactions

## Slide 8: Current Solutions to Disable Screen-off Activities
iOS
Android
Yelp
iOS
Disable useful background activities, affecting user experience
Android
Too cumbersome for users

## Slide 9: Our Goal
Automatically suppress background activities during screen-off that are not useful to users

## Slide 10: Key Hypothesis
Usefulness of app screen-off activities is
  app-dependent
  user-dependent
Intuitive
Validated by real-world data

## Slide 11: Outline
How to quantify usefulness?
  Test the hypothesis
How to develop an online algorithm to optimize screen-off energy?

## Slide 12: Quantify Usefulness: Background-Foreground Correlation (BFC)
Screen-off interval
Screen-on interval
Background activity
Foreground activity
b1
b2
time
2. BFC is the average of
0  low correlation  useless
1  high correlation  useful
1. Define per-interval

## Slide 13: BFC of 2000-User Traces
BFC is app-dependent
  60% of apps have zero BFC
BFC is user-dependent

## Slide 14: Prediction-based Online Algorithm
1. Keep track of per-app BFC for each user using exponential moving average
,
2. Suppress background activities in interval
if

## Slide 15: Evaluation Metrics
1. Energy saving:
2. Staleness:
time
Background activity
Foreground activity

## Slide 16: Evaluation of Prediction-based Online Algorithm
16.4% avg. energy saving (upper bound = 29%)
2.5x staleness increase
Can we improve staleness and maintain energy saving?

## Slide 17: Analysis of High Staleness

## Slide 18: Exponential Backoff Algorithm
time
Original algorithm：
Background activity
Foreground activity
Relax the strictness of suppressing
Exponential backoff：
staleness
time
threshold time:

## Slide 19: Exponential Backoff Algorithm
time
Original algorithm：
Background activity
Foreground activity
Relax the strictness of suppressing
Exponential backoff：
staleness
time
staleness

## Slide 20: Evaluation of Exponential Backoff Algorithm
avg. energy saving 16.4%  15.7%
staleness increase 2.5x 1.3x
staleness of individual apps reduces

## Slide 21: Architecture of HUSH
allowHush
LocationManagerService
TelephoneRegistry
PendingIntentRecord
BroadcastQueue
…
BatteryStatsImpl.Uid.Pkg{
long mBgTime;
long mThrTime;
void updateFg(){…}
void updateBg() {…}
boolean allowHush() {…}
}
ActivityManagerService
BatteryStatsImpl.Uid.Pkg.Serv
updateBg
updateFg
Intercept framework modules to suppress background activities on behalf of apps

## Slide 22: Early Evaluation of HUSH
 | User - 1 |  | User - 2 | 
Number of installed apps | 73 |  | 52 | 
Daily screen-on intervals | 85 |  | 29 | 
Daily screen-on time (min) | 82.35 |  | 49.95 | 
Daily suppressions by HUSH | 4400 |  | 5543 | 
 | Android | HUSH | Android | HUSH
Daily CPU busy time (min) | 164.2 | 97.40 | 60.81 | 27.24
Maintenance power (mA) | 12.76 | 12.76 | 12.12 | 12.12
Avg. screen-off power (mA) | 15.57 | 5.27  | 3.19 | 2.18 
Avg. screen-on power (mA) | 316.8 | 323.5  | 271.4 | 273.0 
Overall avg. power (mA) | 45.50 | 36.34  | 27.32 | 18.99 
3x
1.5x
1.3x
1.4x
2 Users: 3 days with original Android, 3 days with HUSH

## Slide 23: Conclusion
Energy measurement study in the wild
  29% of daily energy due to background activities during screen-off
Quantify usefulness of background activities
  Background-Foreground Correlation
Usefulness is app-dependent and user-dependent
Screen-off energy optimizer: HUSH
  Save 15.7% daily energy on average
  Available at https://github.com/hushnymous/

## Slide 24: Backup

## Slide 26: Features of HUSH
Allow to disable
background suppression
Allow to adjust background
suppression aggressiveness